## Slide 1: SpecDivergence: Mitigating Speculative Execution Attacks through Compiler-Driven Execution Divergence
Ali Hajiabadi, Archit Agarwal, Trevor E. Carlson
National University of Singapore
NUS-CompArch Group Meeting
29th April 2022

## Slide 2: Overview
Speculative Execution Attacks
  Visual Example
Mitigations
  Securing the Side-Channel
  Side-Channel-Agnostic Mitigation
  Compiler-Assisted Side-Channel-Agnostic Mitigation
  Speculation Divergence (SpecDivergence) – our work

## Slide 3: Speculative Execution Attack
unit8 A[10];
uint8 B[256]; //side-channel (SC)
void victim(size_t addr){
if (addr < 10){ //safety check - mispredicts
uint8 val = A[addr]; //accessing secret
uint8 x = B[val]; //transmitting secret to SC
}
}
void attack(){
//Phase 1: initializing the side-channel
for (i = 0; i < 256; i++)
clflush(B[i]);
//Phase 2: running the victim
size_t secret_offset = secret_address - A;
victim(secret_offset);
//Phase 3: recovering the secret
for (guess = 0; guess < 256; guess++){
t1 = rdtscp(); //read timer
temp = B[guess]; //accessing the guess
t2 = rdtscp(); //read timer
if (t2-t1 <= CACHE_HIT_THRESHOLD)
results[guess] += 1; //potential secret
}
}
Spectre V1 using cache side-channel
Setup Phase: Initializing the Side-Channel
The attacker initializes the side-channel to a known state (e.g., all cache lines flushed)
Attacker
Access & Transmit Phase: Running Victim
Victim speculatively accesses the secret and transmits the secret to the side-channel
Victim
Recovery Phase: Probing the Side-Channel
The attacker probes the side-channel to detect the changes done by victim and recover the secret
Attacker
1
2
3

## Slide 4: Execution Example: Spectre on OoO Core
uint8 B[256]; //side-channel (SC)
for (i = 0; i < 256; i++)
clflush(B[i]);
Fetch
Decode
Execute
Commit
R0 | 
R1 | 
R2 | 
COND | 
Register File
Line # | Content
0 | Flushed
1 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache1
Phase 1: Side-Channel Setup
Flushing all the cache lines of the side-channel (cache)
Code Snippet
Array B
Reorder
Buffer

## Slide 5: Execution Example: Spectre on OoO Core
unit8 A[10];
uint8 B[256]; //side-channel (SC)
void victim(size_t addr){
if (addr < 10){ //safety check - mispredicts
uint8 val = A[addr]; //accessing secret
uint8 x = B[val]; //transmitting secret to SC
}
}
Fetch
Decode
Execute
Commit
R0 | 
R1 | 
R2 | 
COND | 
Register File
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Code Snippet
Array B
Reorder
Buffer

## Slide 6: Execution Example: Spectre on OoO Core
victim:
R0 = addr
CMP COND, R0, 10 //branch condition
JG END //mispredicts
R1 = A[R0] //accessing the secret
R2 = B[R1] //transmitting the secret
END: RET
Fetch
Decode
Execute
Commit
R0 = addr
CMP COND, R0, 10
JG END
R1 = A[R0]
R2 = B[R1]
RET
Head
Tail
Reorder Buffer
R0 | addr
R1 | 
R2 | 
COND | 
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Victim Pseudo Assembly Code
Non-speculatively executed
Speculatively executed
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B

## Slide 7: Execution Example: Spectre on OoO Core
victim:
R0 = addr
CMP COND, R0, 10 //branch condition
JG END //mispredicts
R1 = A[R0] //accessing the secret
R2 = B[R1] //transmitting the secret
END: RET
Fetch
Decode
Execute
Commit
R0 = addr
CMP COND, R0, 10
JG END
R1 = A[R0]
R2 = B[R1]
RET
Head
Tail
Reorder Buffer
R0 | addr
R1 | 
R2 | 
COND | X
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Victim Pseudo Assembly Code
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed

## Slide 8: Execution Example: Spectre on OoO Core
victim:
R0 = addr
CMP COND, R0, 10 //branch condition
JG END //mispredicts
R1 = A[R0] //accessing the secret
R2 = B[R1] //transmitting the secret
END: RET
Fetch
Decode
Execute
Commit
R0 = addr
CMP COND, R0, 10
JG END
R1 = A[R0]
R2 = B[R1]
RET
Head
Tail
Reorder Buffer
R0 | addr
R1 | 
R2 | 
COND | X
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Victim Pseudo Assembly Code
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed

## Slide 9: Execution Example: Spectre on OoO Core
victim:
R0 = addr
CMP COND, R0, 10 //branch condition
JG END //mispredicts
R1 = A[R0] //accessing the secret
R2 = B[R1] //transmitting the secret
END: RET
Fetch
Decode
Execute
Commit
R0 = addr
CMP COND, R0, 10
JG END
R1 = A[R0]
R2 = B[R1]
RET
Head
Tail
Reorder Buffer
R0 | addr
R1 | 42
R2 | 
COND | X
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Victim Pseudo Assembly Code
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed

## Slide 10: Execution Example: Spectre on OoO Core
victim:
R0 = addr
CMP COND, R0, 10 //branch condition
JG END //mispredicts
R1 = A[R0] //accessing the secret
R2 = B[R1] //transmitting the secret
END: RET
Fetch
Decode
Execute
Commit
R0 = addr
CMP COND, R0, 10
JG END
R1 = A[R0]
R2 = B[R1]
RET
Head
Tail
Reorder Buffer
R0 | addr
R1 | 42
R2 | X
COND | X
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Victim Pseudo Assembly Code
Line # | Content
0 | Flushed
… | Flushed
42 | Accessed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed

## Slide 11: Execution Example: Spectre on OoO Core
victim:
R0 = addr
CMP COND, R0, 10 //branch condition
JG END //mispredicts
R1 = A[R0] //accessing the secret
R2 = B[R1] //transmitting the secret
END: RET
Fetch
Decode
Execute
Commit
R0 = addr
CMP COND, R0, 10
JG END
RET
Head
Tail
Reorder Buffer
R0 | addr
R1 | X
R2 | X
COND | 0
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel (the secret is 42)
Victim Pseudo Assembly Code
Line # | Content
0 | Flushed
… | Flushed
42 | Accessed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed
Squash &
Re-fetch

## Slide 12: Execution Example: Spectre on OoO Core
for (guess = 0; guess < 256; guess++){
t1 = rdtscp(); //read timer
temp = B[guess]; //accessing the guess
t2 = rdtscp(); //read timer
if (t2-t1 <= CACHE_HIT_THRESHOLD)
results[guess] += 1; //potential secret
}
Fetch
Decode
Execute
Commit
R0 | 
R1 | 
R2 | 
COND | 
Register File
Phase 3: Probing the Side-Channel
The attacker probes all the cache lines of the side-channel to recover the secret.
 Secret (42) is the only one that hits in the cache.
Code Snippet
Line # | Content
0 | Flushed
… | Flushed
42 | Accessed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Reorder
Buffer

## Slide 13
How to mitigate speculative execution attacks?
First solution: Securing the side-channel

## Slide 14: Mitigation Securing the Side-Channel
Fetch
Decode
Execute
Commit
R0 | 
R1 | 
R2 | 
COND | 
Register File
Phase 3: Probing the Side-Channel
The attacker probes all the cache lines of the side-channel to recover the secret.
Line # | Content
0 | Flushed
… | Flushed
42 | Accessed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Reorder
Buffer
This mitigation makes the cache invisible to the attacker  The attacker can’t extract any useful information by observing the cache.
Examples: InvisiSpec[MICRO’18], Delay-on-Miss[ISCA’19], CEASER[MICRO’18] (cache randomization), CleanupSpec[MICRO’19]
Invisible

## Slide 15: Mitigation Securing the Side-Channel
Fetch
Decode
Execute
Commit
R0 | 
R1 | 
R2 | 
COND | 
Register File
Line # | Content
0 | Flushed
… | Flushed
42 | Accessed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Reorder
Buffer
Disadvantage: only secures a specific side-channel
There are various and multiple side-channels (e.g., BTB1)
Invisible
Visible
Question: How to secure all side-channels?

## Slide 16
How to mitigate speculative execution attacks?
First solution: Securing the side-channel
Second solution: Side-channel-agnostic mitigation

## Slide 17: Mitigation Side-Channel-Agnostic Mitigation
Fetch
Decode
Execute
Commit
R0 = addr | 0
CMP COND, R0, 10 | 0
JG END | 0
R1 = A[R0] | 1
R2 = B[R1] | 1
RET | 1
Head
Tail
Reorder Buffer
R0 | addr
R1 | 
R2 | 
COND | X
Register File
Phase 2: Secret Access and Transmit
Victim speculatively accesses the secret and transmits the secret to the side-channel
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed
This mitigation restricts the execution of instructions that can possibly transmit the secret to any side-channel  Restricted instructions will execute only if they become non-speculative.
Restricted?
Restricted because they depend on an unresolved branch
No secret transmitted

## Slide 18: Mitigation Side-Channel-Agnostic Mitigation
Fetch
Decode
Execute
Commit
R0 = addr | 0
CMP COND, R0, 10 | 0
JG END | 0
R1 = A[R0] | 1
R2 = B[R1] | 1
RET | 1
Head
Tail
Reorder Buffer
R0 | addr
R1 | 
R2 | 
COND | X
Register File
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed
Restricted?
Examples: NDA[MICRO’19], STT[MICRO’19], DOLMA[USENIX Sec’21]
Question: Is this solution conservative?
Optimization: Exploiting compiler information to relax unnecessary restrictions

## Slide 19
How to mitigate speculative execution attacks?
First solution: Securing the side-channel
Second solution: Side-channel-agnostic mitigation
Third solution: SW-assistance for the second solution

## Slide 20: Mitigation Software-Assisted Side-Channel-Agnostic Mitigation
Insight: Not all instructions in ROB are dependent to the most recent branch1,2
Fetch
Decode
Execute
Commit
Branch | 0
dependent | 1
Independent | 0
dependent | 1
Head
Tail
Reorder Buffer
R0 | 
R1 | 
R2 | 
COND | 
Register File
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Non-speculatively executed
Speculatively executed
Restricted?
Communicating non-speculative dependency information
Compiler Static Analysis
Marks branch dpdendent instructions
1
Enhanced HW Mitigation
Lifts execution restrictions from any instruction independent from the branch
2

## Slide 21: Results Software-Assisted Side-Channel-Agnostic Mitigation
Core configuration: 8-issue, 32 LQ/SQ entries, 192 ROB entries, Tournament BP
L1i / L1d / L2 / L3 Cache: 32KB, 32KB, 256KB, 1MB
Mitigation mode: Memory + Register protection
Core | Overhead over Baseline
 | (M+R) mode
STT | 37.0%
DOLMA | 32.3%
DOLMA-CI | 15.1%

## Slide 22: Mitigation Side-Channel-Agnostic Mitigation
Fetch
Decode
Execute
Commit
R0 | 
R1 | 
R2 | 
COND | 
Register File
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Array B
Non-speculatively executed
Speculatively executed
Branch | 1
dependent | 1
Independent | 0
dependent | 1
Head
Tail
Reorder Buffer
Restricted?
Disadvantage: Still many components in the core keep speculative state and can serve as a side-channel
Vulnerability Example: Intentionally executing independent vs. dependent instructions and use ROB contention as a side-channel (Speculative Interference Attacks)1,2
Speculative state

## Slide 23
How to mitigate speculative execution attacks?
First solution: Securing the side-channel
Second solution: Side-channel-agnostic mitigation
Third solution: SW-assistance for the second solution
Forth solution: Speculation Divergence (SpecDivergence)

## Slide 24: Mitigation SpecDivegrence
BB1
Normal OoO Execution
BB2
BB3
BB4
Unresolved Branch
Solution: Prediction and speculative fetch/execution
Execution Flow:
BB1
BB2
BB4
BB3
BB4
Branch
Misprediction
SpecDivergence Execution
BB1
BB2
BB3
BB4-Dependent
Unresolved Branch
BB4-Independent
Execution Flow:
BB1
BB4-Independent
BB3
BB4-Dependent
Branch
Branch resolves
Solution: Non-speculative fetch/execution of independent instructions
BB1
BB2
BB4
BB3
BB4
Misprediction
BB1
BB3
Branch resolves
BB4-Dependent
BB4-Independent

## Slide 25: Mitigation SpecDivergence
Insight: No speculative state kept in any component
Solution: Exploiting compiler information to introduce non-speculative paths
Fetch
Decode
Execute
Commit
Branch
Independent
Resolved Dependent
Head
Tail
Reorder Buffer
R0 | 
R1 | 
R2 | 
COND | 
Register File
Line # | Content
0 | Flushed
… | Flushed
42 | Flushed
… | Flushed
255 | Flushed
… | …
512 | ….
Cache
Non-speculatively executed
Speculatively executed
Implementation: Compiler informs the core about the alternative paths and the fetch unit redirects the fetch based on compiler information
Fetch
Compiler
Alternative paths for each branch

## Slide 26: Mitigation SpecDivergence Scheduling Algorithm
Execution modes:
  Normal
    Nomral OoO execution
  SpecDivergence_Diverged
    Executing independent instruction after a branch
  SpecDivergence_Original
    Executing dependent instructions after a branch
Gem5 Implementation in progress

## Slide 27: SpecDivergence Mitigating Speculative Execution Attacks through Compiler-Driven Execution Divergence
Thanks for your attention
Questions?